## Slide 1: Satellite System Architecting
Problem: Assign instruments to Orbits OCE_SPEC
Instrument | Description
ACE_ORCA | Ocean color spectrometer
ACE_POL | Aerosol Polarimeter
ACE_LID | Differential absorption lidar
CLAR_ERB | SW+LW Radiation Budget
ACE_CPR | Cloud & Precipitation radar
DESD_SAR | Polarimetric L-band SAR
DESD_LID | Vegetation/ice green lidar
GACM_VIS | UV/VIS limb spectrometer
GACM_SWIR | SWIR nadir spectrometer
HYSP_TIR | SWIR-TIR hyperspectral imager
POSTEPS_IRS | IR atmospheric sounder
CNES_KaRIN | Wide-swath radar altimeter
Orbit | Description
LEO 600 Polar | Polar orbit in low earth orbit (600km)
SSO 600 AM | Sun synchronous orbit with local time of the ascending node (LTAN) in the morning (600km)
SSO 600 DD | Sun synchronous orbit with LTAN at dawn and dusk (600km)
SSO 800 PM | Sun synchronous orbit with LTAN in the afternoon (800km)
SSO 800 DD | Sun synchronous orbit with LTAN at dawn and dusk (800km)
Objective: Find the best Pareto front
Task: Try to improve an architecture by adding instruments using given information and any other pattern you notice along the way
  You will be given a random architecture
  Add instruments to it and submit it
  After submitting, you will get to see the science score and cost
  Try to increase science score and reduce cost
  Find non-dominated solutions

## Slide 2: Expert Knowledge (based on previous experiments) Good Features:
3~5 occupied orbits
  5 orbits -> high science and cost
  4 orbits -> best without SSO 600 DD
  3 orbits -> best with 1 polar orbit and 2 SSO orbits
10~15 total instruments using 9 out of the 12 available instruments
Architectures with more than 24 instruments is invalid
HYSP_TIR in polar orbit
GACM_VIS in PM orbit
POSTEPS_IRS in AM or PM orbit
ACE_ORCA in AM orbit
ACE_ORCA not in DD orbit
ACE_POL not in DD orbit
VACM_VIS not in DD orbit
GACM_SWIR not in DD orbit